## Slide 1
LAB LOGO
JULY 2026 PROGRESS UPDATE
NS-3 Traffic QoS Model & Hybrid Switching Reliability
Hybrid Network Construction and Performance Evaluation for Multi-Robot Systems at Construction Sites
Presented by
Sheikh Sayed Bin Rahman
PIC Lab, Kyushu Institute of Technology (KIT)
NS-3.45 · WiFi Mesh + LTE / 5G NR
Replace the top-left box with the PIC Lab logo

## Slide 2
LAB LOGO
What was completed in July
Software implementation and reliability fixes for the NS-3 hybrid simulator
1
QoS traffic model
Replaced generic traffic with Control, Sensor, and Video flows, each with DSCP marking.
2
Per-flow measurement
Added flow_metrics.py for Control PDR, P99 latency, and throughput share.
3
WiFi association crash fix
Patched stale Association Response handling so multi-AP roaming no longer aborts NS-3.
4
Switch recovery improvement
Recovery confirmation now uses Control UDP, improving resolved-switch rate on test cases.
5
Multi-seed evaluation
Completed a 5G NR matrix across seeds 6/7/8 and STA counts 5/10/15.
Sheikh Sayed Bin Rahman · PIC Lab, Kyushu Institute of Technology (KIT)
2 / 8

## Slide 3
LAB LOGO
July deliverable — robot traffic QoS model
Three application flows with independent FlowMonitor measurement
Control
• UDP, ~1 KB / 50 ms
• DSCP EF (robot commands)
• Target: P99 ≤ 50 ms
• Loss target: 0%
Sensor
• TCP telemetry upload
• DSCP AF31
• Target: delay ≤ 200 ms
• Loss target: < 5%
Video
• TCP continuous stream
• DSCP AF41
• Target: delay ≤ 500 ms
• Loss target: < 10%
Deliverable status
Artifact | Role | Status
traffic_qos.cc | NS-3 scenario with 3-flow traffic + DSCP | Complete
flow_metrics.py | Per-flow PDR / delay / P99 / throughput | Complete
traffic_qos_report.pdf | Full statistical analysis report | Pending 192 runs
Sheikh Sayed Bin Rahman · PIC Lab, Kyushu Institute of Technology (KIT)
3 / 8

## Slide 4
LAB LOGO
WiFi BSSID crash — root cause and fix
NS-3 aborted under multi-AP roaming with shared SSID MeshHotspot
1
Associate
STA requests association to AP 0c
2
Roam
Missed beacons → rescan → new request to AP 0b
3
Stale frame
Delayed AssocResp from abandoned AP 0c arrives
4
Crash
Assert: target BSSID ≠ response BSSID
Correction in sta-wifi-mac.cc
Ignore Association Responses whose BSSID does not match the STA’s current target AP. Keep waiting for the correct response instead of aborting the simulation.
4 / 9
runs crashed before
9 / 9
runs complete after
0
aborts in re-sweep
Sheikh Sayed Bin Rahman · PIC Lab, Kyushu Institute of Technology (KIT)
4 / 8

## Slide 5
LAB LOGO
Switch recovery confirmation improved
Representative case: 5G NR · 10 STA · seed 7 · 60 seconds
What changed
Recovery was previously confirmed only when Sensor TCP traffic resumed. TCP can stall after a route rewrite, so many successful handovers were counted as timeouts. Recovery is now confirmed from the continuous Control UDP flow, and stale pending switch events are retired when a newer path decision occurs.
Before
57%
resolved switches 20 timeouts out of 47 events median interruption 178 ms
After
87%
resolved switches 2 timeouts out of 47 events median interruption 55 ms
Full 9-run matrix (all seeds/STA): 73% overall resolved · WiFi→NR 88% · NR→WiFi return 57%
Note: return from cellular to WiFi is still harder than the forward WiFi→NR path; multi-seed data is required for the report.
Sheikh Sayed Bin Rahman · PIC Lab, Kyushu Institute of Technology (KIT)
5 / 8

## Slide 6
LAB LOGO
Seeds and STA count still matter
Same code, same 60 s / 5G NR setup — different RNG seeds change outcomes
Seed | STA | Switches | Resolved | Timeout | Timeout % | Median ms
6 | 5 | 24 | 14 | 6 | 25% | 65
6 | 10 | 60 | 42 | 8 | 13% | 61
6 | 15 | 96 | 72 | 16 | 17% | 245
7 | 5 | 23 | 15 | 4 | 17% | 564
7 | 10 | 47 | 41 | 2 | 4% | 55
7 | 15 | 84 | 62 | 13 | 15% | 63
8 | 5 | 34 | 29 | 2 | 6% | 39
8 | 10 | 60 | 50 | 6 | 10% | 52
8 | 15 | 78 | 45 | 18 | 23% | 557
Best: seed 7 / 10 STA (4% timeout). Worst: seed 6 / 5 STA (25%). A single seed would have overstated reliability — hence the 192-run campaign.
Sheikh Sayed Bin Rahman · PIC Lab, Kyushu Institute of Technology (KIT)
6 / 8

## Slide 7
LAB LOGO
Next: 192-run campaign for the formal report
Phase 1 factorial design with the July QoS traffic model
The remaining July analysis deliverable is traffic_qos_report.pdf. It needs a full multi-factor campaign, not single-run results.
Factor | Values | Levels
Cellular mode | LTE, 5G NR | 2
WiFi hotspot band | 2.4 GHz, 5 GHz | 2
STA count | 5, 10, 15, 20 | 4
Payload / load | 10 KB, 50 KB, 1 MB, 2 MB | 4
RNG seed | 6, 7, 8 | 3
Total | 2 × 2 × 4 × 4 × 3 | 192 runs
Campaign outputs
• Control PDR and P99 tables
• LTE vs NR comparison
• Switch interruption statistics
Report goal
• Seed-averaged KPIs
• Factor-level confidence
• traffic_qos_report.pdf
Sheikh Sayed Bin Rahman · PIC Lab, Kyushu Institute of Technology (KIT)
7 / 8

## Slide 8
LAB LOGO
Thank You
Questions and discussion are welcome.
Sheikh Sayed Bin Rahman
PIC Lab, Kyushu Institute of Technology (KIT)
Hybrid Robot Network Simulator · NS-3.45
Replace the top-left box with the PIC Lab logo